## Slide 1
Quantification of Uncertain Effects in Engineering Systems
UKACM & GACM Autumn School 2025 Open-Source Codes for High-Performance Computing Hands-on Session 4C & QUEENS
Sebastian Brandstäter1, Maximilian Dinkel2, Lea Häusel2, Jonas Nitzler2, Gil Robalo Rei2
1 Institute for Mathematics and Computer-Based Simulation | University of the Bundeswehr Munich
2 Institute for Computational Mechanics | Technical University of Munich

## Slide 2: QUEENS
is a Python framework for solver-independent multi-query analyses of large-scale computational models.
https://github.com/queens-py/queens

## Slide 3: Multi-Query Analysis
Examples of multi-query scenarios:
Open loop: parameter studies, uncertainty quantification
Closed loop: optimization, (Bayesian) inverse problems
Evaluation of the same model at many input locations
Input 1
Model
Output 1
Input 2
Model
Output 2
Input N
Model
Output N
Input i
Model
Output i
i:=i+1

## Slide 4: Automation of model evaluations
Each model evaluation involves numerous time-consuming manual sub-steps, e.g.,
Model
Input i
Output i
Preprocessing
Simulation
Postprocessing
QUEENS offers an abstract framework to automate all of these sub-steps.

## Slide 5: Run 4C with a single line of code
Input template.4C.yml
Essentially, everything you need is:
model.evaluate(dens=[2,10])
Run 4C on HPC
cluster
Run 4C on HPC
cluster
Input file for density=10
Input file for density=2

## Slide 6: Available analysis methods
parameter studies and identification
sensitivity analysis
surrogate modelling
(multi-fidelity) uncertainty quantification
Bayesian inverse analysis
A large variety of methods that are likely to be relevant to your research
Methodological complexity
QUEENS offers a large collection of cutting-edge algorithms for deterministic and probabilistic analyses:

## Slide 7: Large-scale computational models
QUEENS is designed for the analysis of computational models in which a single evaluation requires significant computational resources.
It provides a modular architecture for:
parallel queries of large-scale computational models
robust data, resource, and error management
easy switching between analysis types
smooth scaling from laptop to HPC cluster

## Slide 8: Solver-independence
It has also been interfaced with other solvers
any Python package
OpenFOAM
Fenics
deal.II-based codes
and many others …
However, QUEENS is developed as a solver-independent platform.

## Slide 9: You are welcome to join! Connect with us on GitHub.
Sebastian Brandstäter
Maximilian Dinkel
Jonas Nitzler
Gil
Robalo Rei
Maintainer team
Lea Häusel
Daniel Wolff
Regina Bühler
Silvia Hervás Raluy
Community
Bishr Maradni
https://github.com/queens-py/queens
Contributors

## Slide 10: Workflow example
Multi-query algortihm
Model
Experiment
Parameters
Evaluation
Compute

## Slide 11: Theory and background
Since some of you might not be familiar with probabilistic approaches…
We will first cover some theory and background to:
Motivate the use of probabilistic approaches
Explain the key concepts behind the hands-on examples
Don’t worry—we’ll keep the math to a minimum.
You’ll revisit these concepts during the tutorial, and most importantly, you’ll be able to follow the exercises even if some of the theory feels challenging.

## Slide 12: What are uncertainties?
Can arise from inherently random effects
Can arise from lack of information/knowledge
External forces:
loads q(x)?
Material parameters: Young's modulus E(x)?
Geometry: cross section A(x)?
Boundary conditions: support type?
Uncertainty is the lack of certainty about a quantity because it has more than one possible state

## Slide 13: Why should I care about uncertainties?
To make meaningful predictions, uncertainty needs to be incorporated:
Every model is only an approximation of reality
Uncertainty through model
Even if a model is perfect, numerically precise results can be meaningless if model parameters are not known precisely
Uncertainty through parameters
With uncertainties, we can tell what we know, but also what we do not know.

## Slide 14: How to handle uncertainties?
How engineers used to handle uncertainties:
  Redo analysis or measurements, analyse mean and standard deviation
  Propagation of significant figures
  Propagation of tolerances
  Post process data (filters, interpolation, ...)
  Use of safety factors
  Playing around with input parameters
Probabilistic approach:
  Use probability theory to describe uncertainty
  Use random variables to model uncertain parameters
Systematic approach

## Slide 15: What are random variables?
For example, is a model parameter:
Random variables:
can assume many values, but with varying probability.
probability density
Deterministic:
assumes a single value.

## Slide 16: What are random fields?
Random variables:
A random variable is a single random number. can assume many values, but with varying probability.
Random field:
A random field is the extension to functions: instead of a random number, you get a whole random function. Each realization of a random field is just one specific function.

## Slide 17: Advantages of probabilistic approaches
Information Quality
How precise can we measure?
precise
imprecise
System Preferences
Are there multiple preferred configurations?
bimodal
mean
single mode
mean
Interactions
Is there a correlation of parameters?
Two-dimensional distribution
nonlinear interactions between and
And many more…

## Slide 18: How to quantify uncertainties?
Uncertainty Propagation
Forward Uncertainty Quantification (UQ)
Quantification of uncertainties in the output
Inverse Analysis (IA)
Backward Uncertainty Quantification (UQ)
Quantification of uncertainties in the input
Forward UQ
Backward UQ
Outputs
Time
Inputs
Model
Parameter 1
Parameter 2
Unknown
Update
Inputs
Parameter 1
Parameter 2
Outputs
Output
Model
Unknown

## Slide 19: Forward Uncertainty Quantification
Known:
  Probability density function of uncertain model inputs
  Model
Unknown:
  Probability density function of uncertain output
is the Dirac mass delta.
Inputs
Parameter 1
Parameter 2
Outputs
Output
Model
Unknown
Goal:
Propagate uncertainties from input quantities to output quantities using a computational model ℳ

## Slide 20: Beam example - deterministic
Model
Where models a static Euler-Bernoulli beam:
Outputs
bending line
Inputs
load

## Slide 21: Forward UQ – Beam example
Inputs
load
Model
Where models a static Euler-Bernoulli beam:
Outputs
bending line
Unknown
Variance smaller towards support

## Slide 22: Bayesian inverse analysis / Backward UQ
Known:
  Observations e.g. from experiments
  Prior over uncertain model inputs
  Model
  Optional but desirable: Model derivative
Unknown:
  Posterior over uncertain model inputs
Outputs
Time
Inputs
Model
Parameter 1
Parameter 2
Unknown
Update
Goal:
Given experimental data and a model ℳ, estimate the unknown input quantities and the uncertainty in this estimate
Bayes‘ rule:

## Slide 23: Bayesian inverse analysis – Beam example
Inputs
Prior :
Outputs
bending line
Observations
Model
Where solves:
Posterior :
Unknown